Square Subarea
Time limit: 1 sec
Given a grid of R row and C column, we can identify each cell in the grid by a coordinate (r,c) where (1 <= r <= R and 1 <= c <= C). A square subarea in a grid, defined by the coordinate (r1,c1) and a size k, is every cell (r,c) such that (r1 <= r <= r1+k-1) and (c1 <= c <= c1+k-1). Assume that each cell contains either a number 0 or 1, you task is to find the largest square subarea that every cell in the sub area is number 1.
For example, the largest square subarea in the following grid has size 3, identified by an underlined 1. Notice that there are also another subarea having size 3 as well.
0 0 0 1 0
0 1 1 1 1
0 0 1 1 1
0 0 1 1 1
0 0 1 1 1
# Input
- The first line contains two integers R and C which are the number of rows and columns of the grid. (1 <= R <= 1000 and 1 <= C <= 1000).
- The following R lines gives the number in the grid. Each lines corresponds to a rows in the grid, starting from row 1 to row R. For each line, there a string of '0' and '1' of length C. Each character in the string represents a value in each cell in the corresponding row, starting from column 1 to column C.
# Output
The output contains a single integer representing the size k of the largest square subarea.
# Example
Input	Output
5 / 00010 / 01111 / 00111 / 00111 / 00111	3
1 10 / 1111111011	1